## Slide 1: Image j
免費影像分析軟體

## Slide 2: Image j
Quantify protein bands
Count cell number
Measure wound healing area
Calibrate scale bar; add scale bar

## Slide 3: Quantify protein bands
File  Open  開啟tif.檔
Image  Type  32-bit

## Slide 4: Quantify protein bands
Image  Adjust
 Brightness/Contrast
Click “Auto

## Slide 5: Quantify protein bands
Select the area to be analyzed
Analyze  Gels  Select First Lane

## Slide 6: Quantify protein bands
Drag box to 2nd lane
Repeat the procedure until all bands selected

## Slide 7: Quantify protein bands
Analyze  Gels  Plot Lanes
Isolate each peak


## Slide 8: Quantify protein bands
Click each area to get value

## Slide 9: Count cell number
File  Open  cell count.jpg
Edit  Options  Conversions

## Slide 10: Count cell number
Check “Scale When Converting”
OK
Image  Type  16-bit

## Slide 11: Count cell number
Image  Adjust  Threshold
Adjust threshold until you are satisfied Apply

## Slide 12: Count cell number
To separate two overlapping cells
Process  Binary  Watershed

## Slide 13: Count cell number
Analyze  Analyze Particles

## Slide 14: Count cell number
Check cell size and circularity

## Slide 15: Count cell number
Plugins  Analyze  Cell Counter

## Slide 16: Count cell number
click “Remove” to remove other cell types.
 Initialize  Keep Original

## Slide 17: Count cell number
Click “Type 1”
Click on cells to count

## Slide 18: Wound healing
File  Open jpg.
Process Enhance Contrast

## Slide 19: Wound healing
Process Smooth
Process Find Edges

## Slide 20: Wound healing
Image  Adjust  Threshold  Apply

## Slide 21: Wound healing
Click each area to get value

## Slide 22: Calibrate scale bar
File  Open jpg.
Zoom in  Draw the scale line

## Slide 23: Calibrate scale bar
Analize  Set Scale
Set known Distance Unit  OK

## Slide 24: Add scale bar
Analize  Tools  Scale Bar
Set Width Color  Location

## Slide 25
~THANK YOU~
Notes: 4